Photovoltaic system - {system:name} / {system:postcode} - {system:city}
Monthly report
Peak Power	{system:performance} kWp
Period	{ep:month} {ep:year}

# Energy yield
1.1 Overview of reporting month

In {mdMonth:calc.month} the solar park generated a total amount of {mdMonth:calc.E_ZAEHLER} kWh. Accordingly, the specific production of the installed capacity was {mdMonth:calc.E_N} kWh/kWp.

The reporting month was characterized by a global radiation (at the module level) of {mdMonth:ad.G_M0} Wh/m² .

	Production		Irradiation
	Energy measured (kWh)	Energy in function of Meter (kWh)	(Wh/m²)
{ep:month} {ep:year}	{mdMonth:calc.E_MESS}	{mdMonth:calc.E_ZAEHLER}	{mdMonth:calc.E_GM}
Year {mdYear:calc.year}	{mdYear:calc.E_MESS}	{mdYear:calc.E_ZAEHLER}	{mdYear:calc.E_GM}

1.2 Overview of the current year
In the year {ep:year} the solar park generated a total amount of electricity of {mdYear:calc.E_ZAEHLER} kWh. Accordingly, a specific production of {mdYear:calc.E_N} kWh/kWp could be achieved so far.
In the operating year 2018, a global radiation of {mdYear:ad.G_M0} Wh/m² was determined for the plant location by the irradiation sensor installed at module level.

The following table summarize the daily values as well as the monthly sum of the current month:
- Energy Production: Produced energy of the PV plant in kWh, measured at the energy meter.
- Specific Yield: The energy production normalised to the installed peak power of {system:performance} kWp.
- Insolation: Solar irradiance in module plane measured by the on-site installed sensors. If more than one sensor is installed the average of the measurement is calculated. The insolation values between 0 and 4 AM are neglected. The insolation to the specification in yield reports has to be referenced to pyranometers which are installed in module plane. The difference of the insolation measured by pyranometers and crystalline sensors is typically 3–5 %.

The actual yields of the PV plant for the current month and current year are opposed to the rated yield values based on simulations of the monitoring portal. The automated simulation takes the plant configuration (modules, inverters, mounting system) and the measured insolation into account. The automated simulation cannot replace a yield report for the considered time period.
Time period	Actual yield	Rated yield by a simulation
current month ({mdMonth:calc.month})	{mdMonth:calc.E_ZAEHLER} kWh	{mdMonth:sim.E_Z_EVU} kWh
current year ({mdYear:calc.year})	{mdYear:calc.E_ZAEHLER} kWh	{mdYear:sim.E_Z_EVU} kWh

# Key Performance Indicators

Performance Ratio:

The Performance Ratio equals the quotient of the specific yield and the insolation in module plane. For the system {system:name} the calculation of the PR is based on the values of {pr:energySource} for the specific yield and as well as the {pr:irradiationSource} for the insolation. The aggregation for the monthly value is based on the {pr:aggregation}.

If the insolation is not measured with a pyranometer but with crystalline sensors, one has to take into account that the PR will be overestimated. Furthermore, the monthly PR cannot be compared the annual PR as the PR depends on seasonal fluctuations. An annual performance check is recommended for a analysis of PR and yield.

The performance Ratio for {mdMonth:calc.month} is {mdMonth:calc.PR} %

Plant Availability:
The Availability of the plant is calculated in respect to the equations defined in the O&M contract. For {mdMonth:calc.month} the system reached an availability in order of {mdMonth:calc.VFG} %.
Therefore the insolation threshold value is {systemAvailability:irradianceThreshold}.

# Yield prognosis and actual/rated yield comparison
3.1 Monthly chart
The following chart represents a comparison of rated and actual yield in the current month. The bars show the daily energy production of the plant. The yellow crosses represent the rated yield based on a daily yield calculation taking the plant configuration and the insolation into account.
- If the measured energy is in the range 90% - 115% compared to the simulation value, the system runs very well (green).
- If the measured energy is in the range 70% - 90% compared to the simulation value, the system runs satisfactorily (yellow).
- If the measured energy is in the range 0% -70% compared to the simulation value, the system must be checked (red).
For a more precise representation, the three calculated areas are first plotted as a superimposed area in the graphic. Depending on the area in which the plant is located, the color of the diagram is also adjusted accordingly and compared with the simulation value. The simulation itself is currently carried out once, if all measured data are already available in the database and takes into account the following input parameters: global irradiance, solar generator, inverter and loss factors.

3.2 Yearly chart
The following chart represents a Comparison of the actual yield (red curve) and the rated yield (yellow curve) as well as the yield prognosis of the plant (blue curve) based on a yield report with long-term insulation data.

  1. Tabular view
In the following table the specific actual yield of the plant is compared to the rated yield based on a yield report. The rated yield has been calculated by a yield simulation taking the long-term insolation into account. The real insolation of a considered time period can fluctuate for each operating year.
Month	Specific actual yield	Specific yield of yield report
{START}{ep:month}.{ep:year}	{ep:SpecificYield} kWh/kWp	{ep:YieldForecast} kWh/kWp{END}

# Tabular views of the energy production
Monthly and yearly values:

	Energy production	Spec. yield	Insolation
{START}Sum {mdMonth:calc.month}	{mdMonth:calc.E_ZAEHLER} kWh	{mdMonth:calc.E_N} kWh/kWp	{mdMonth:calc.E_GM} Wh/m²
Sum {ep:year}	{mdYear:calc.E_ZAEHLER} kWh	{mdYear:calc.E_N} kWh/kWp	{mdYear:calc.E_GM} Wh/m² {END}

Daily values

	Energy production	Spec. yield	Insolation
{START}{mdDay:calc.date}	{mdDay:calc.E_ZAEHLER} kWh	{mdDay:calc.E_N} kWh/kWp	{mdDay:calc.E_GM} / Wh/m²